## Slide 1: TurboVent:
A turbine-based ventilator design

## Slide 2: Simple Idea  Few Parts
Brushless DC Motor + Drive Electronics
Turbine Impeller + Enclosure
Pressure Sensor
2 Flow Sensors
PEEP Valve
Processor + Software
User Interface

## Slide 3: Overall Circuit Diagram
Motor/Turbine
Flow
Sensor
Flow
Sensor
Pressure
Sensor
Peep
Valve
Air In
(need to add FiO2 mixing)
Ventilator
Patient
Circuit

## Slide 4: Motor/Impeller Requirements
Brushless DC motor (BLDC) for controllability.
Small, to enable quick response (motor diameter 15mm – 25mm).
To deliver required pressure/volume:
  High Speed: EG. 50,000 – 60,000 RPM
  High Power
High speed requirements lead to impeller balance issues?

## Slide 5: Candidate Motors
Maxon ECX SPEED 19mm motor
  Manufacturer has confirmed availability
Nidec-copal TF037E micro-blower
  Availability unknown, this includes impeller, and would simplify design work
Hoover OnePwr Blade Max vacuum blower
  Would include impeller, simplifying design
  Commercial product would ensure availability of sufficient numbers
  Would require cooperation from a large company

## Slide 6: Other parts
NXP Differential Pressure Sensor: https://www.nxp.com/docs/en/data-sheet/MPXV7002.pdf
B&B AccuTach PneumoTach Flow Sensor: http://bandb-medical.com/accutach-pneumotach-flow-sensor/
Superior Sensing Pressure Sensor: https://www.digikey.com/product-detail/en/superior-sensor-technology-inc/HV120-SM02-R/2232-HV120-SM02-RCT-ND/10647412
Carefusion Airlife Adjustable PEEP Valve: https://www.medicaleshop.com/carefusion-airlife-adjustable-peep-valves-with-22mm-i-d-connection-and-22mm-adapter-each.html?source=ppc&gclid=Cj0KCQjwjoH0BRD6ARIsAEWO9DsOjHAKk43FBICgp7WY_prjf86tJY5z1SeKZmH2RDHQzL2ptbB0cqwaAmGIEALw_wcB